## Slide 1: Process Diagram
실병투입 (분석가)
반출입기
분석기
Stocker
분석기
Full?
N
Y
실병
실병
실병
분석
완료?
재검병
실병 OR 재검병
폐기설비
공병
재검 대기만료 병
N
Y
공병회수 (분석가)
분석기가 분석 중에도 실병/재검병 투입이 가능한가?
Stocker나 반출입기가 Full이 되어 MoMa가 움직일 수 없는 상황에 대한 대처 방안은?
Stocker에 재검 대기 병이 너무 많아 Capa가 부족해지는 경우는?
MoMa 대기는 MoMa가 1대인 경우, 전체 프로세스가 정지됨
MoMa가 대기 상태가 되면, 반출입기나 Stocker에서 Capa를 수동으로 확보하여야 함 (혹은 반출입기를 임시 Stocker로 활용  재검병도 임시로 반출입기에 저장???)
Stocker
Full?
N
Y
Stocker
Full?
N
Y
MoMa 대기
분석완료병
재검병 OR 분석완료병
MoMa 대기
반출입기
Full?
실병
실병
N
Y
재검병
대기
분석가 결정

## Slide 2: Pick & Put Actions at Nodes (Except MoMa)
Node | Actions | 실병 | 분석완료병 | 재검대기병 | 공병
InOutBot | Pick | ✓ |  |  | 
 | Put |  |  |  | ✓
Stocker | Pick | ✓ | ▲(2) | ✓ | ▲(3)
 | Put | ✓ | ▲(4) | ✓ | ▲(5)
Analyzer | Pick |  | ✓ | ✓ | 
 | Put | ✓ |  |  | 
Disposer | Pick |  |  |  | ✓
 | Put | ▲(1) | ✓ | ✓ (대기시간만료) | 
반출입기에 입고된 실병을 분석 안하고, 폐기  간혹 발생됨
분석기에서 분석이 완료(재검 없음)된 분석완료병을 Stocker에 잠시 대기  Disposer가 Full인 경우에 발생 가능하나, Disposer에 여유 Capa가 있으므로 거의 발생 안됨
Disposer에서 세척 완료된 공병을 Stocker에 잠시 보관  반출입기가 Full인 경우에 발생 가능하나, Disposer에 여유 Capa가 있으므로 거의 발생 안됨
2번과 같은 경우
3번과 같은 경우

## Slide 3: Status Definition of Each Nodes
Subjcet | Status 1 | Status 2 | Status 3 | Status 4 | Status 5 | Status 6 | Status 7
Bottle Pack | Filled (실병) | Empty (공병) | Complete (분석완료) | Waiting (재검대기) | Disposed (폐기) | Missing | Reserved
반출입기 | On/Off | Busy | Idle | Error | Maintenance | Full | Reserved
분석기 | On/Off | Busy | Idle | Error | Maintenance | Full | Reserved
Stocker | On/Off | Busy | Idle | Error | Maintenance | Full | Reserved
폐기설비 | On/Off | Busy | Idle | Error | Maintenance | Full | Reserved
MoMa | On/Off | Busy | Idle | Error | Maintenance | - | Reserved
폐기설비는 Full이 될 가능성은 낮음